## Slide 1
AEROTHON 2026 - HAL x IITI
Team Name: Zypher
Participants: Anurag | IIT Indore Aerothon 2026

## Slide 2
SERIES-HYBRID VTOL CHALLENGE
PROBLEM UNDERSTANDING & MOTIVATION
• MTOW: 1,000 kg | Payload: 200 kg | Cruise: 250 km/h • Altitude: 3,000–10,000 m | VTOL capability required • Goal: maximise endurance while meeting all HAL constraints
Page 1

## Slide 3
LITERATURE REVIEW / EXISTING APPROACHES
Page 2
STATE OF THE ART
• Conventional VTOL: pure electric — limited endurance (~45 min) • Existing hybrids: parallel architecture adds weight & complexity • Our approach: series-hybrid with optimal power-split

## Slide 4
PROPOSED METHODOLOGY & TECHNICAL APPROACH
Page 3
PHYSICS-FIRST OPTIMIZATION
• 5-phase mission: VTOL → Climb → Cruise → Loiter → Descent • Actuator-disk VTOL model + ISA atmosphere (0–10 km) • Sobol quasi-random sampling → Pareto-optimal design front

## Slide 5
DATA SOURCES & PREPROCESSING
Page 4
MISSION PARAMETERS
• HAL constraints: 1,000 kg MTOW, 200 kg payload, 250 km/h cruise • Physics model: battery (250 Wh/kg), engine (60 kW, BSFC 0.26), structure (3.8 kg/m²) • ML training data: 2,000 physics simulation samples

## Slide 6
MODEL ARCHITECTURE / IMPLEMENTATION PLAN
Page 5
SYSTEM ARCHITECTURE
• Physics engine: ISA density, drag (CD=0.025), battery SOC (4.4C max) • Pareto optimizer: Sobol sampling, 500 designs, endurance vs mass trade-off • ML dispatcher: MLPRegressor predicts engine/battery kW split in real time

## Slide 7
EXPECTED OUTCOMES & EVALUATION METRICS
Page 6
KEY RESULTS
• Reference design: 1,000 kg MTOW | 17.9 h endurance | 0 violations • Best endurance: 50.4 h (44.8 kWh, 152.9 kg fuel, 940 kg) • Power-split: engine at 85% rated (optimal BSFC) during climb, idles in cruise

## Slide 8
TEAM COMPOSITION & CONTRIBUTIONS
Page 7
TEAM ZYPHER
• Anurag: Physics modeling, optimizer, ML dispatcher, dashboard • Faculty Mentor: IIT Indore Department of Aerospace Engineering • All source code: github.com/Techie551/HAL-VTOL-Hybrid-Optimizer

## Slide 9
APPENDIX & REFERENCES
APPENDIX
• Source code: github.com/Techie551/HAL-VTOL-Hybrid-Optimizer • Interactive dashboard: streamlit run dashboard.py • Unit tests: PYTHONPATH=. python -m unittest tests.test_series_hybrid -v