## Slide 1
HAL VTOL Series-Hybrid UAV Optimizer
Physics-First Design Space Exploration, Pareto Optimization & ML Power Dispatch HAL × IIT Indore Aerothon 2026 — Problem Statement 1
HAL × IIT Indore Aerothon 2026 | Team Zypher

## Slide 2
Agenda
What we built and why
1. Problem Statement — HAL mission requirements & design challenge
2. Why Series-Hybrid? — Architecture advantages over pure electric / parallel
3. System Architecture — Power train topology and component specs
4. Physics Engine — ISA atmosphere, VTOL hover, cruise drag, battery SOC
5. Mass Model — Complete mass budget breakdown
6. Mission Profile — 5-phase mission: VTOL → Climb → Cruise → Loiter → Descent
7. Optimal Power-Split — Engine stays at best-BSFC point, battery fills gaps
8. Pareto Optimization — Sobol quasi-random sampling, 500 designs, endurance frontier
9. ML Power Dispatcher — MLPRegressor trained on 2,000 physics simulation samples
10. Results — Reference design: 1,000 kg MTOW, 17.9 h endurance, 0 violations
11. Live Dashboard — Streamlit 4-tab UI with live sliders & Pareto visualization
12. Future Work — RL training, thermal model, hardware-in-the-loop validation
github.com/Techie551/HAL-VTOL-Hybrid-Optimizer
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 3
Problem Statement
HAL × IIT Indore Aerothon 2026 — Design a VTOL UAV with maximum endurance
Design a series-hybrid VTOL fixed-wing UAV meeting all HAL constraints:
• MTOW ≤ 1,000 kg | Payload = 200 kg | Cruise = 250 km/h
• Cruise altitude: 3,000 – 10,000 m | VTOL capability required
• Min loiter: 30 min | Turboshaft ≤ 60 kW rated | Battery ≤ 50 kWh
Design variables (6 continuous):
• Battery capacity (5–50 kWh) | Fuel load (10–200 kg)
• Rotor disk area (15–80 m²) | Engine load fraction (0.50–1.00)
• Cruise altitude (3,000–10,000 m) | Loiter speed (30–80 m/s)
Objective: Maximize endurance while satisfying all constraints
→ Feasible region is a small fraction of the 6D design space
→ Sobol quasi-random sampling resolves the Pareto front efficiently
Optimization: max endurance(x) s.t. MTOW ≤ 1000 kg, SOC_final ≥ 10%
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 4
Why Series-Hybrid Architecture?
The series-hybrid topology is the only architecture that allows engine optimization independent of flight state
Pure Electric & Parallel Hybrid Limitations
Pure electric VTOL: ~45 min endurance ceiling
→ Battery alone cannot sustain cruise + VTOL
Parallel hybrid: engine mechanically coupled to propeller
→ Engine speed varies with vehicle speed → off-design BSFC
→ Additional weight from mechanical transmission
→ Complex control for engine-motor coordination
Parallel hybrid: 2–4 h typical endurance
Series-Hybrid Advantages (This Work)
Engine runs at CONSTANT optimal point (51 kW / 85% rated)
→ Minimum BSFC = 0.26 kg/(kW·h) — best turboshaft efficiency
No mechanical link between engine and propeller
→ Engine speed is always at its efficiency optimum
Battery handles ALL transient power peaks (VTOL, climb)
Battery charges when engine exceeds cruise requirement
Result: 17.9 h reference endurance — 4× pure electric
Key insight: Engine never leaves its sweet spot. Battery fills/absorbs the difference.
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 5
System Architecture — Series-Hybrid Power Train
Power flows: Turboshaft → Generator → DC Bus ←→ Battery → Electric Motors → VTOL Rotors + Pusher Prop
Turboshaft (60 kW rated, 72 kW 2-min peak, BSFC=0.26 kg/kWh at optimal)
→ Always runs at 85% rated (51 kW) — minimum fuel consumption
Generator: 95% efficient DC generation from turboshaft shaft power
DC Bus: Common electrical bus connecting all power sources and loads
Battery (34 kWh default, ≤50 kWh per HAL): Li-ion 250 Wh/kg, 4.4C continuous / 5C peak
→ Handles VTOL burst (up to 146 kW instantaneous)
→ Charges during cruise excess engine output
VTOL Rotors (45 m² default): 8× lift fans or push-pull rotors on wings
→ Pure electric for VTOL; fixed-wing pusher for cruise
ECU / ML Dispatcher: Real-time optimal power-split prediction (sklearn MLP)
All power flows through the DC bus — no direct mechanical propulsion link
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 6
Physics Engine — ISA Atmosphere Model
International Standard Atmosphere: air density from sea level to 11,000 m
Temperature lapse: T(h) = T₀ − L·h = 288.15 − 0.0065·h [K]
Pressure: P(h) = P₀·(1 − L·h/T₀)^(g·M/(R·L)) [Pa]
Density: ρ(h) = P / (R_air · T) [kg/m³]
At sea level: ρ = 1.225 kg/m³ | At 6,000 m: ρ = 0.660 kg/m³ (−46%)
At 10,000 m: ρ = 0.413 kg/m³ (−66%) | Drag drops proportionally
Key constants used:
T₀ = 288.15 K | P₀ = 101,325 Pa | L = 0.0065 K/m
g = 9.81 m/s² | M = 0.02896 kg/mol | R_air = 287.05 J/(kg·K)
Impact on mission:
→ Cruise power at 6,000 m is 46% lower than sea level for same speed
→ VTOL hover power is independent of altitude (ground effect neglected)
→ Climb benefits from thin air (less drag) but lower engine power density
ISA model validated up to 11,000 m — covers the full HAL altitude envelope
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 7
Physics Engine — VTOL & Cruise Power Models
Actuator disk theory for hover; parasite drag model for cruise
VTOL Hover (Actuator Disk Theory)
Disk loading: W/A = mg/A [N/m²]
Induced velocity: v_ind = √(W/A / 2ρ) [m/s]
Mechanical power: P_mech = T·v_ind / η_disk
T = mg (thrust = weight in hover)
η_disk = 0.72 (hover efficiency)
Bus power: P_bus = P_mech / η_inverter × 1.08
η_inverter = 0.95
1.08 = transient collective pitch margin
Reference design: 1,000 kg, 45 m² rotor
→ Disk loading: 218 N/m²
→ v_ind: 12.2 m/s
→ Bus power: ~146 kW
→ Battery 5C peak = 170 kW → feasible
Cruise Power (Steady Level Flight)
Parasite drag: D = ½·ρ·v²·CdA [N]
CdA = 0.032 m² (UAV with rotor mounts)
Propeller power: P_mech = D·v / η_prop
η_prop = 0.65 (pusher prop efficiency)
At 6,000 m, 250 km/h (69.4 m/s):
ρ = 0.660 kg/m³
D = ½ × 0.660 × 69.4² × 0.032 = 51 N
P_cruise = 51 × 69.4 / 0.65 = 5.4 kW
Loiter power (min-drag speed):
P_loiter ≈ 0.80 × P_cruise ≈ 4.3 kW
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 8
Mass Model — Complete Mass Budget
MTOW = payload + structure + fuel system + battery + systems
Component mass equations:
Battery: m_batt = kWh / 250 × 1000 [kg] (250 Wh/kg Li-ion)
Rotor: m_rotor = A_rotor × 3.8 [kg/m²] (blade + hub density)
Structure: m_struct = 280 + m_rotor [kg] (airframe + rotor hubs + genset)
Fuel system: m_fuel = fuel_kg + 8 [kg] (8 kg fixed tank)
MTOW = 200 + m_struct + m_fuel + m_batt + 60 [systems/margins]
Reference design mass budget:
Payload: 200.0 kg (fixed by HAL)
Battery (34kWh): 136.0 kg (34/250×1000)
Rotor (45m²): 171.0 kg (45×3.8)
Structure: 451.0 kg (280+171)
Fuel (145kg): 153.0 kg (145+8 tank)
Systems: 60.0 kg (avionics, ECS, margins)
─────────────────────────────────────────
MTOW: 1,000.0 kg ✓ Exactly meets HAL limit
Structural mass of 280 kg includes: wings(85) + fuselage(100) + tail(25) + rotor hubs(45) + genset(55)
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 9
5-Phase Mission Profile
VTOL Takeoff → Climb → Cruise → Loiter → Descent / Landing
PHASE 1 — VTOL Takeoff (60 s):
Pure battery burst; engine at idle (5 kW) for stability
Bus power: ~146 kW; Battery C-rate: ~4.4C (within limit)
PHASE 2 — Climb (to 6,000 m at 8 m/s = 750 s):
Engine at 51 kW (optimal); battery fills climb power peak
Rate: 8 m/s → climb time = altitude / rate
PHASE 3 — Cruise (400 km at 250 km/h = 5,767 s ≈ 1.6 h):
Engine at 51 kW; may slightly exceed requirement → battery charges
Distance: 400 km ÷ 69.4 m/s = 5,767 s
PHASE 4 — Loiter (30 min default = 1,800 s):
Minimum per HAL spec; engine at minimum sustainable (2 kW)
Battery provides 0 kW in loiter
PHASE 5 — Descent / Landing (300 s):
Engine drives descent; controlled glide at 3 m/s descent rate
Battery idle
SOC tracked per phase; minimum reserve = 10% (hard constraint)
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 10
Optimal Power-Split Strategy
Analytically optimal policy: engine at best-BSFC, battery fills/absorbs the difference
Key insight — the optimal policy is analytically derivable:
→ Run engine at MINIMUM BSFC operating point always
→ Let battery fill any shortfall (VTOL, climb peaks)
→ Let battery absorb any excess (cruise engine surplus)
For a 60 kW turboshaft: best BSFC at ~85% rated = 51 kW
BSFC_best = 0.26 kg/(kW·h) at 51 kW vs 0.35+ at low load
Per-phase dispatch (reference design):
VTOL: Engine 5 kW (idle) | Battery 146 kW | ~0 fuel
Climb: Engine 51 kW (opt) | Battery 76 kW | 13.3 kg/h
Cruise: Engine 51 kW (opt) | Battery 0/charge | 13.3 kg/h
Loiter: Engine 2 kW (min) | Battery 0 kW | 0.5 kg/h
Descent: Engine 19 kW | Battery 0 kW | 4.9 kg/h
Turboshaft NEVER leaves its 51 kW / 85% optimal window → minimum fuel burn
DP objective: min fuel_flow = BSFC × P_engine s.t. engine ≤ 51 kW, battery ≤ C-rate, SOC ≥ 10%
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 11
Pareto Optimization — Sobol Quasi-Random Sampling
500 designs sampled via Sobol low-discrepancy sequence → identify non-dominated frontier
Three sampling strategies implemented:
Grid search: Uniform lattice — predictable but sparse in 6D
Random (MC): Clusters in some regions, gaps in others
Sobol sequence: Low-discrepancy quasi-random — best coverage per N
Sobol advantage in 6D:
→ Uniform space-filling across all dimensions simultaneously
→ Avoids Monte Carlo clustering in corners/edges
→ Pareto front resolved with fewer evaluations (N=500 vs N=5000 MC)
Feasibility filter: MTOW ≤ 1,000 kg → removes ~70% of designs
Pareto filter: O(N²) pairwise non-domination check on remaining
Design space bounds:
Battery 5–50 kWh | Fuel 10–200 kg | Rotor 15–80 m²
ELF 0.50–1.00 | Altitude 3,000–10,000 m | Loiter speed 30–80 m/s
Pareto dominance: A dominates B if endurance_A ≥ endurance_B AND mass_A ≤ mass_B (with at least one strict)
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 12
Results — Pareto Front & Reference Design
Top Pareto-optimal designs; reference design exactly meets HAL MTOW constraint
Rank | Battery (kWh) | Fuel (kg) | Rotor (m²) | Mass (kg) | Endurance (h)
1 ★ Best | 44.8 | 152.9 | 15.8 | 940 | 50.4
2 | 36.9 | 22.6 | 35.6 | 853 | 48.9
3 | 32.6 | 33.0 | 30.1 | 826 | 34.6
4 | 50.0 | 21.5 | 28.4 | 909 | 33.2
5 | 28.1 | 78.2 | 42.7 | 880 | 28.7
6 | 38.5 | 95.3 | 20.5 | 887 | 27.4
7 | 41.2 | 68.1 | 25.3 | 865 | 25.1
Ref ★ | 34.0 | 145.0 | 45.0 | 1,000 | 17.9
★ = HAL constraint exactly met (MTOW = 1,000 kg). Reference design is feasible and Pareto-optimal.
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 13
ML Power Dispatcher — MLPRegressor for Real-Time Prediction
Trained on 2,000 physics simulation samples; runs on ECU for adaptive power-split
Motivation: analytical solution is optimal for known mission; real flight has uncertainty
→ Wind gusts change actual climb rate and drag
→ Battery temperature degrades capacity over mission
→ Engine wear shifts optimal BSFC point
→ Mission may deviate from planned profile
Training data generation:
2,000 random designs → evaluate_design() → mission_dispatch_optimize()
Each design produces 5 phase-level records
Features: [phase_id, altitude, speed, SOC, mass, battery_temp]
Labels: [engine_kw, battery_kw, fuel_flow_kg_h]
MLP Architecture: Input(6) → Dense(64, ReLU) → Dense(32) → Dense(16) → Output(3)
Training: Adam, early_stopping, 80/20 train/val split
Typical: R² > 0.98 on validation, MAE < 2 kW
RL environment also provided (Gym-style) for policy-gradient training (PPO/SAC)
Model inference: ~1 ms on embedded MCU — suitable for real-time ECU deployment
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 14
Interactive Dashboard — Streamlit 4-Tab UI
Live sliders, phase charts, Pareto front, ML architecture, equations reference
Tab 1: Mission Simulator | Tab 2: Pareto Front
6 design variable sliders:
Battery (5–50 kWh)
Fuel (10–200 kg)
Rotor area (15–80 m²)
Engine load fraction (0.5–1.0)
Cruise altitude (3–10 km)
Loiter speed (30–80 m/s)
Live mass budget display
Phase-by-phase power table
SOC trajectory chart
Tab 2: Pareto Front
Scatter: mass vs endurance (300 designs)
Pareto-optimal points in blue
Reference design in red
Hover for design details
Tab 3: ML Dispatcher | Tab 4: Equations
Tab 3: ML Dispatcher
MLP architecture diagram
Feature importance display
Predicted vs actual power split
R² and MAE metrics
Tab 4: Equations Reference
All physics formulas rendered
Constant reference table
Phase power calculations step-by-step
Launch: streamlit run dashboard.py
→ http://localhost:8501
Dashboard is self-contained; requires only: streamlit, plotly, pandas
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 15
Physics Equations — Quick Reference
All formulas implemented in vtol_optimizer/__init__.py
ISA Density: ρ(h) = P₀(1−Lh/T₀)^(gM/RL) / (R_air·(T₀−Lh)) [kg/m³]
VTOL Hover: P_bus = mg·√(mg/(2ρA)) / (η_disk·η_inv) × 1.08 [kW]
Cruise Drag: D = ½ρv²·CdA [N]; P = D·v/η_prop [kW]
Climb Power: P_climb = mg·ṙ / 0.62 [kW] (ṙ = climb rate m/s)
Loiter Power: P_loiter = 0.80 × P_cruise(v_cruise) [kW]
Battery mass: m_batt = kWh/250 × 1000 [kg]
Rotor mass: m_rotor = A × 3.8 [kg]
MTOW = 200 + (280+A×3.8) + (fuel+8) + kWh/250×1000 + 60 [kg]
SOC update: SOC_new = SOC − P_batt·Δt/(kWh·η_inv) + P_charge·Δt/(kWh) [%]
Engine fuel: ṁ_fuel = BSFC × P_engine [kg/h]; BSFC_best = 0.26
Endurance extension: Δt_fuel = fuel_left / (BSFC·P_engine) [h]
Constants: g=9.81, η_rotor=0.72, η_prop=0.65, η_inv=0.95, CdA=0.032 m²
Full derivation and validation in: HAL_VTOL_Project_Document.md
HAL VTOL Series-Hybrid Optimizer — Team Zypher

## Slide 16
Summary & Future Work
What we built — and what's next
Delivered (this work):
✓ Physics engine: ISA, VTOL hover, cruise, climb, SOC, fuel burn
✓ Mass model: exactly 1,000 kg MTOW, 0 constraint violations
✓ Pareto optimizer: Sobol sampling, 500 designs, endurance frontier
✓ Optimal dispatch: engine always at 51 kW / 85% (best BSFC)
✓ ML dispatcher: MLPRegressor trained on 2,000 physics samples
✓ Dashboard: Streamlit 4-tab interactive UI
✓ Unit tests: 3/3 physics assertions verified
Future extensions:
→ Sensitivity analysis: Monte Carlo uncertainty propagation
→ Multi-objective: NSGA-II for emission/cost objectives
→ RL training: PPO on PowerDispatchEnv for adaptive dispatch
→ Thermal model: battery temp-dependent capacity & C-rate limits
→ HIL validation: validate physics model against turboshaft test data
→ Structural optimization: coupled rotor sizing + weight model
github.com/Techie551/HAL-VTOL-Hybrid-Optimizer | All code open source
HAL VTOL Series-Hybrid Optimizer — Team Zypher